## Slide 1
On-Premise Hyperscale Pod Designs
Modular Architecture for Big Data Deployments & Container Convergence
Infrastructure Specification Blueprint

## Slide 2
Core Architectural Pillars
Disaggregated Shared-Everything (DASE): decoupling compute from storage to scale capacity and processing limits independently.
Isolated Traffic Fabrics: dedicated physical lanes split big data shuffle streams away from critical storage read/write paths.
Cross-Cabinet Resiliency: distributed software architecture handles individual hardware failures cleanly without data corruption risks.
Compute Nodes: standard dual-socket servers, 32 Core / 64 Thread servers containing 1TB RAM to process heavy runtime queries.
Central Storage Cluster: a highly optimised VAST Data configuration deployed across a leaf / spine architecture supporting a 13PB raw / 39PB (3:1 DRR) flash matrix.
Distributed High Availability: splitting transactional databases and stateless storage entities across separate power and/or POD boundaries .

## Slide 3
Pod Sizing & Power Profiles - 3 Rack Design
Option A: 15 kW Mid-Density (CR-B)
• Supports 50 compute nodes across a 3 cabinets.
Operates within a safe continuous power ceiling.
Utilizes 64-port high-density network switches.
Option B: 5 kW Low-Density (WDC H1)
• Stacks 24 total compute nodes into 3 cabinets.
• Maximizes computing capacity for low kW infrastructure.
• Wired via standard 36-port leaf switches.
Option A: 15 kW Mid-Density (CR-B)
• Supports 38 compute nodes across a 2 cabinets.
Operates within a safe continuous power ceiling.
Utilizes 64-port high-density network switches.
Storage: Per POD Design
4 cabinet solution
Supports 2 D-Nodes 2.2PB usable per cabinet
Supports 4 C-Nodes per cabinet
2 Dedicated VAST Data Leaf switches per cabinet
2 Dedicated VAST Data Spine switches co-located with HSBC cores

## Slide 4
Pod Sizing & Power Profiles - 2 Rack Compute Design
Option A: 15 kW Mid-Density (CR-B)
• Supports 38 compute nodes across a 2 cabinets.
Operates within a safe continuous power ceiling.
Utilizes 64-port high-density network switches.
Option B: 5 kW Low-Density (WDC H1)
• Stacks 24 total compute nodes into 2 cabinets.
• Maximizes computing capacity for low kW infrastructure.
• Wired via standard 36-port leaf switches.
Storage: 15 kW Mid-Density (CR-B)
3 cabinet solution
Supports 4 D-Nodes 4.4PB usable per cabinet
Supports 6 C-Nodes per cabinet
2 Dedicated VAST Data Leaf switches per cabinet
2 Dedicated VAST Data Spine switches co-located with HSBC cores
Storage: 5 kW Low-Density (CR-B)
4 cabinet solution
Supports 2 D-Nodes 2.2PB usable per cabinet
Supports 4 C-Nodes per cabinet
2 Dedicated VAST Data Leaf switches per cabinet
2 Dedicated VAST Data Spine switches co-located with HSBC cores

## Slide 5
Storage Matrix: VAST Data Integration
13.2 PB Usable (39.6PB with 3:1 DRR) Flash Infrastructure: managed through a decoupled software-defined layout.
Stateless VAST CNodes (Compute Elements): 24 total nodes distributed evenly across all cabinets (1 per rack). Handles processing and protocol abstraction safely.
VAST DNodes (Data Units): 2 highly dense hardware shelves located in each POD to handle bulk files natively.
VAST S3 API providing high performance storage for Big Data processing via Apache Spark, Hive, Trino processing engines.
VAST Block CSI Operator: attaches volumes via automated Virtual IP (VIP) addresses over NVMe/TCP paths.
VAST Filesystem CSI: grants active container structures simultaneous shared access (ReadWriteMany) to big data folders.
Efficiency Maintenance: structural metadata compression lowers actual capacity costs across the cluster.

## Slide 6
High Availability Database Architecture
PostgreSQL Bare-Metal Cluster: deployed across all 3 racks to eliminate single points of power failure.
Failover Management: uses an independent consensus network layer to orchestrate cluster states.
Automated Promotion Flow: moves primary master roles to surviving nodes in under 30 seconds if a rack drops offline.
Dual MaxScale Proxies: serve as highly resilient network entry points to mask node adjustments from the application layer.
Smart Routing Layout: connection pools divide write traffic away from read queries dynamically.
Converged Interconnect: interfaces connect directly to the compute switches via secure, isolated VLAN paths.

## Slide 7
Network Fabric & Cabling Rules
Intra-Rack Media: short Direct Attach Copper (DAC) cables provide high efficiency and lowest latency.
Inter-Rack Media: thin Active Optical Cables (AOC) pass through overhead pathways to ensure crisp airflow.
Switch Distribution Setup: compute leaves are split across cabinets 1 and 2, while storage leaves run via MLAG links in cabinet 3.
Jumbo Frames Implementation: standard MTU limits are set to 9000 across all interfaces to lower parsing overheads.
Lossless Flow Control: enabling PFC and ECN settings completely stops packet drop incidents during massive shuffles.
Bandwidth Performance Guardrails: isolated VLAN mappings protect data workloads from network interference.

## Slide 8
Convergence Roadmap: Hadoop to K8S
Phase 1: Storage Decoupling
• Transition application lines to use S3 API or VAST native storage drivers.
• Eliminates local disk dependencies on data workers.
Phase 2: Modern Schedulers
• Deploy the Spark-on-K8S Operator inside the cluster.
• Bypasses legacy YARN processing engines completely.
Phase 3: Hardware Re-Provisioning Flow
• 1. Safe drainage of leftover Hadoop workload tasks.
• 2. Automated network PXE boots to wipe system drives.
• 3. Fresh installation of the minimal operating image.
• 4. Deployment of the Kubelet runtime agent.
• 5. Node automatically registers as a fresh compute asset.

## Slide 9
Disaster Recovery (DR) Strategy
Cross-Site VAST Snapshot Streaming: snapshots pass natively over WAN paths between Site A and Site B data centers.
Data Reduction Retention: global deduplication patterns are maintained during transit to lower WAN network bills.
Asynchronous Database Syncing: continuous transaction logs stream into a dedicated Patroni Standby environment.
Unified Failover Runbook Flow:
• 1. Update Global Traffic routing entries to swing client access towards Site B.
• 2. Signal Patroni at Site B to promote its standby database node to full Primary mode.
• 3. Trigger the VAST CSI Operator to mount replicated files, allowing containers to immediately resume query tracking.