## Slide 1
On-Premise Hyperscale Pod Designs
Modular Architecture for Big Data Deployments & Container Convergence
Infrastructure Specification Blueprint

## Slide 2
Core Architectural Pillars
Disaggregated Shared-Everything (DASE): decoupling compute from storage to scale capacity and processing limits independently.
Isolated Traffic Fabrics: dedicated physical lanes split big data shuffle streams away from critical storage read/write paths.
Cross-Cabinet Resiliency: distributed software architecture handles individual hardware failures cleanly without data corruption risks.
Compute Nodes: standard dual-socket servers containing 1TB RAM to process heavy runtime queries.
Central Storage Cluster: a highly optimized VAST Data configuration supporting a 20PB raw flash matrix.
Distributed High Availability: splitting transactional databases and stateless storage entities across separate power boundaries.

## Slide 3
Pod Sizing & Power Profiles
Option A: 15 kW Mid-Density
• Supports 31 compute nodes across a 3-rack limit.
• Operates with a 12.0 kW safe continuous ceiling.
• Wired via standard 36-port leaf switches.
Option C: 7 kW Corporate Low-Density
• Supports 13 compute nodes across the pod mesh.
• Restricts continuous drawer load to 5.6 kW.
• Fits perfectly in non-specialized server rooms.
Option B: 30 kW Extreme-Density
• Stacks 67 total compute nodes into 3 cabinets.
• Maximizes computing capacity within a 24.0 kW continuous line envelope.
• Utilizes 64-port high-density network switches.
• Requires specialized infrastructure tools like Rear Door Heat Exchangers (RDHx) to handle intense thermal loads.

## Slide 4
Storage Matrix: VAST Data Integration
20PB Raw Flash Infrastructure: managed through a decoupled software-defined layout.
Stateless VAST CNodes (Compute Elements): 3 total nodes distributed evenly across all cabinets (1 per rack). Handles processing and protocol abstraction safely.
VAST DNodes (Data Units): 2 highly dense hardware shelves located in Rack 3 to handle bulk files natively.
VAST Block CSI Operator: attaches volumes via automated Virtual IP (VIP) addresses over NVMe/TCP paths.
VAST Filesystem CSI: grants active container structures simultaneous shared access (ReadWriteMany) to big data folders.
Efficiency Maintenance: structural metadata compression lowers actual capacity costs across the cluster.

## Slide 5
High Availability Database Architecture
PostgreSQL Bare-Metal Cluster: deployed across all 3 racks to eliminate single points of power failure.
Patroni Failover Management: uses an independent consensus network layer to orchestrate cluster states.
Automated Promotion Flow: moves primary master roles to surviving nodes in under 30 seconds if a rack drops offline.
Dual MaxScale Proxies: serve as highly resilient network entry points to mask node adjustments from the application layer.
Smart Routing Layout: connection pools divide write traffic away from read queries dynamically.
Converged Interconnect: interfaces connect directly to the compute switches via secure, isolated VLAN paths.

## Slide 6
Network Fabric & Cabling Rules
Intra-Rack Media: short Direct Attach Copper (DAC) cables provide high efficiency and lowest latency.
Inter-Rack Media: thin Active Optical Cables (AOC) pass through overhead pathways to ensure crisp airflow.
Switch Distribution Setup: compute leaves are split across cabinets 1 and 2, while storage leaves run via MLAG links in cabinet 3.
Jumbo Frames Implementation: standard MTU limits are set to 9000 across all interfaces to lower parsing overheads.
Lossless Flow Control: enabling PFC and ECN settings completely stops packet drop incidents during massive shuffles.
Bandwidth Performance Guardrails: isolated VLAN mappings protect data workloads from network interference.

## Slide 7
Convergence Roadmap: Hadoop to K8S
Phase 1: Storage Decoupling
• Transition application lines to use S3 API or VAST native storage drivers.
• Eliminates local disk dependencies on data workers.
Phase 2: Modern Schedulers
• Deploy the Spark-on-K8S Operator inside the cluster.
• Bypasses legacy YARN processing engines completely.
Phase 3: Hardware Re-Provisioning Flow
• 1. Safe drainage of leftover Hadoop workload tasks.
• 2. Automated network PXE boots to wipe system drives.
• 3. Fresh installation of the minimal operating image.
• 4. Deployment of the Kubelet runtime agent.
• 5. Node automatically registers as a fresh compute asset.

## Slide 8
Disaster Recovery (DR) Strategy
Cross-Site VAST Snapshot Streaming: snapshots pass natively over WAN paths between Site A and Site B data centers.
Data Reduction Retention: global deduplication patterns are maintained during transit to lower WAN network bills.
Asynchronous Database Syncing: continuous transaction logs stream into a dedicated Patroni Standby environment.
Unified Failover Runbook Flow:
• 1. Update Global Traffic routing entries to swing client access towards Site B.
• 2. Signal Patroni at Site B to promote its standby database node to full Primary mode.
• 3. Trigger the VAST CSI Operator to mount replicated files, allowing containers to immediately resume query tracking.